## Slide 1: Information and Communication Technologies – Basic Terms
Ing. Simona Kubíková, PhD.
Department of Road and Urban Transport
University of Žilina
Žilina, Slovakia

## Slide 2
What Does Information Mean?
Data
Information
Knowledge
Information leads to an increase in understanding and decrease in uncertainty.
Information is valuable because it can affect behavior, a decision, or an outcome.

## Slide 3
Information System
Collecting data
Storing data
Processing data
Distributing data
Information system also includes people, technical means and methods which ensure collecting, processing and storing data for presenting this information to users.

## Slide 4
Software – suitable information system, apps and security
Hardware – computers, printers, cameras, etc.
Peopleware – employees, external users
Orgware – legislature, laws
Dataware – sources of data and information, databases
Elements of Information System

## Slide 5
Structure of Information System
Collecting data
Processing data
Distributing data
Information transfer
Collecting data: measuring (sensors and detectors, meteo-stations,...); verbal (police, public, drivers); databases (restrictions, public transport)
Processing data: dispatch centres, centres of traffic information
Distributing data: provide individually (GSM,WAP), available for public (radio, RDS/TMC, variable message signs)

## Slide 6
Static – one direction process of information, f.e. radio broadcasting, RDS/TMC, GSM
Dynamic – both direction process of information, where a vehicle provides information about its position. A centre of transport information can provide information to this vehicle directly; it is short range transfer
Information Systems in Road Transport
Source of information
Processing system
Source of information
Processing system

## Slide 7
Acoustic and optic – radio broadcasting, navigation, VMS
Whole traffic flow – VMS
Inside a vehicle – RDS/TMC, navigation
Information Systems in Road Transport

## Slide 8
Important characteristics of information:
  Real time
  Valuable
  Credible
  Accurate
Drivers' willingness to accept provided information is crucial!!
Information Systems in Road Transport

## Slide 9
Information is provided by information boards near a road or by portal over a road (variable message signs).
Information about traffic accidents, congestions, obstacles on roads, delays, bad weather conditions, tunnel closures, etc.
Traffic Flow Information Systems

## Slide 10
Information is automatically generated in NTIC
Critical parameters are intensity and speed of traffic flow
Bi-directional communication is needed
Control unit has continuous power source which provides information transfer about defects and system's failures
Communication is provided by metal or optical line
GSM/SMS and radio connection
Traffic Flow Information Systems

## Slide 11
1. Vehicle works as a ,,floating vehicle“
which sends information about its position.
Providing information via radio transmission.
Vehicle should be equipped with an on-board unit
Information Systems in Vehicles

## Slide 12
Active information system
  Vehicle sends information about its position to the control centre.
  Control centre sends relevant information about traffic situation, congestions, restrictions, etc., within the driver' s chosen route
  Communication between a vehicle and a centre is ensured f.e. by DSRC
Information Systems in Vehicles

## Slide 13
Active Information System
Information Systems in Vehicles
Central management
Traffic Data
Transmitter
Information for driver
Local management

## Slide 14
Information Systems in Vehicles
Passive Information System
  One-way communication
  Vehicle does not send information about its position
  Vehicle only receives information about traffic situation from traffic centre
  GSM, RDS/TMC

## Slide 15
Information Systems in Vehicles
Real - Time Information about Traffic Accidents
  Choose an alternative route
  Avoid traffic accident, congestions and delays
  Modern trends – electronic recorder of accident (30 sec before TA and 15 sec after); recording speed, acceleration, direction and characteristics of vehicle

## Slide 16
Information Systems in Vehicles
Real - Time Information about speed and occurrence of danger
  Traffic sensors and detectors measuring speed (radars)
  VMS – sharp curve, dangerous intersection
  Main goal - decrease a number of traffic accidents caused by high speed and breach of traffic regulations

## Slide 17
Information Systems in Road Transport
  Benefits:
    Increasing traffic safety,
    Reducing uncertainty in decision making – traffic situation
    Decreasing time delays
    Effective using of road communication network
    Reducing drivers' stress behaviour
    Reducing negative impacts on environmental
    Accident cost savings
    Operating cost savings

## Slide 18
National System of Transport Information
  Basic requirements for NSTI implementation:
    Increase mobility and quality of transport services
    Minimizing congestions
    Increase effectiveness of transportation
    Provide real time information to road users
    Reduce emissions and fuel consumption
    Increase quality of life and environment
The main aim of NSTI is to ensure better traffic flow fluency and traffic safety.

## Slide 19
National System of Transport Information
  includes National Traffic Information Centre
    Central, technological, operational and organising part of NSTI
    ensures collecting, confirming, processing, and providing traffic information
    Providing information – telecommunication channels, RDS/TMC, web pages, etc.
    Gathering information from road users, police, owner and administrator of road network, administrator of fee collection, meteorological stations, etc.

## Slide 20
National System of Transport Information

## Slide 21
Communication Systems in Road Transport
Transfer of information and providing to road users, using telecommunication networks
Fixed communication networks – wireless and wired networks
Mobile communication networks – satellite and ground systems
Requirements for safety, reliability and availability of information transmission
No requirements
Requirements
Any environment
Special networks

## Slide 22
GSM (Global System for Mobil Communication)
  First standard GSM published in 1990
  Area divided to cells with different frequencies
  Multiple using of assigned frequencies – follow the rule of distances between each cells which use the same frequency
Communication Systems in Road Transport

## Slide 23
GSM (Global System for Mobil Communication)
  Driver sends an SMS with his route on a predefined telephone number and in a moment he receives information about traffic situation.
  Possible to use GSM for vehicle tracking in real time but only if GPS is available.
Communication Systems in Road Transport

## Slide 24
Communication Systems in Road Transport
DSRC (Dedicated Short Range Communication)
  Wireless system based on microwaves or infra-red transmission
  Transmission for short ranges
  High resistance of bad weather conditions
  Using within active safety (avoidance of traffic accidents occurrence, ambient sensing, communication V2V and V2I)

## Slide 25
Communication Systems in Road Transport
DSRC (Dedicated Short Range Communication)
  System of emergency warning of vehicles in front
  Adaptive cruise control
  Cooperative caution of collision in front of a vehicle
  Caution of complicated junction
  Controlling of vehicle safety
  Electronic payment for parking
  Electronic fee collection
  Railway crossing warning

## Slide 26
Communication Systems in Road Transport
RDS/TMC (Radio Data System/ Traffic Message Channel)
RDS
  Communication protocol standard for embedding small amounts of digital information in conventional FM radio broadcasts
  Digital information are showed on radio display
TMC
  Specific application of FM RDS used for broadcasting real-time traffic and weather information.
  Data messages are received silently and decoded by a TMC-equipped navigation system, and delivered to the driver
  Offering dynamic route guidance – alerting the driver of a problem on the planned route and calculating an alternative route to avoid the incident

## Slide 27
Communication Systems in Road Transport
TMC
  Standard TMC user messages provide five basic items of broadcast information: event description, location, direction and extent, expected duration, diversion advice
  Benefits:
Updated traffic information, delivered in real time
Instant knowledge of accidents, roadworks and traffic jams
Filtered information only for the immediate route
Information in user’s own language
High-quality digital transmission
Standardised compatibility of receivers
Widespread service delivery

## Slide 28
Communication Systems in Road Transport

## Slide 29
Communication Systems in Road Transport
TPEG (Transport Protocol Experts Group)
  offer a method for transmitting multimodal traffic and travel information, regardless of client type, location or required delivery channel (e.g. DAB, HD radio, Internet, DVB-x, DMB, GPRS, Wi-Fi) and it is language independent.
  TPEG applications:
    Road Traffic Message (RTM)
    Public Transport Information (PTI)
    Traffic Event Compact (TEC)
    Traffic Flow and Prediction (TFP)
    Parking Information (PKI)
    Weather Information (WEA)
    Congestion and Travel Time (CTT)

## Slide 30
Communication Systems in Road Transport

## Slide 32
Variable message signs
https://www.youtube.com/watch?v=KsRvAIoLd-s
https://www.youtube.com/watch?v=LeqjFHbZ0J4
https://www.youtube.com/watch?v=WCECCoQzY5o
RDS -TMC
https://www.youtube.com/watch?v=PLKh_tLWdlI
https://www.youtube.com/watch?v=cPalrA2DeTg
https://www.youtube.com/watch?v=24tgONHEbSM HERE traffic

## Slide 33
Simona.Kubikova@fpedas.uniza.sk
Department of Road and Urban Transport
University of Žilina
Žilina, Slovakia
Thank you for your attention.