## Slide 1: Basic terms of ITS with focusing on transport problems (Lecture 1)
assoc. prof. Ing. Jaroslav Mašek, PhD.
Department of Railway Transport, FPEDaS

## Slide 2: 1. Basic terms of ITS with focusing on transport problems - content
Goal: Student will understand base terms of modelling the transport processes
Teaching methods: lecture, presentation
Support material: PC, data projector, presentation
Content: Definition of main terms – transport, transportation, process, carrier, transport contractor, transport element, set, requisites, hub, throughput, capacity, route, track, relation, course, queue, center, etc...
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 3: 2. Basic terms of ITS with focusing on transport problems
Transport is intentional movement (driving, sailing, flight) of transport means along transport routes or activity of transport equipment by which the transportation is performed. According to relocated objects, we distinguish between passenger and cargo transport. The subject of transport in general terms may also be different media (gases, liquids), electricity or even information.
Transport is closely related to the means of transport and the transport route, as the relocation is usually carried out by the means of transport along the road. That is not always the case as, for example, in pedestrian transportation there are no means of transport used and for certain modes of transport (balloon flights), the routes of transport have not to be precisely defined.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 4: 2. Basic terms of ITS with focusing on transport problems
Transportation is an activity by which is directly affected a movement of persons and things (goods) using vehicles or transport facilities.
In accordance with these terms, the carrier is the transport operator, while the customer is an organisation or a person who receives a product/service and who requests the relocation of the object. If the carrier and customer are the same legal entity or natural person, it is an independent or autonomous transport. All types of public transport are among non-autonomous transport.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 5: 2. Basic terms of ITS with focusing on transport problems
Transport can be classified according to different aspects, e.g.:
according to environment (land, underground, water, air),
according to transport road (road, rail, river, sea, air, pipeline, conveyor, cableway and other),
according to means of transport (walking, cycling, automobile, tramway, trolleybus, railway, etc.).
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 6: 2. Basic terms of ITS with focusing on transport problems
The general theory of transport is a summary of concepts and knowledge of transport, which generalizes the specific characteristics of each mode of transport. It is closely related to logistics, which is comprehensively understood as the theory of circulatory processes, considered mainly from an economic point of view. The subject of transport theory is the study of the patterns of movement of particular objects on transport networks or the examination of transport technology.
Technology refers to a summary of the organization, transport means and methods of working of machinery and people whose actions change the value of these objects. Technological processes can be improved in two ways: innovation of technical means or innovation of an organization. One of the main goals of transport theory is to innovate the organization and management of the movement of transport means and transport flows along the transport network.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 7: 2. Basic terms of ITS with focusing on transport problems
Transport element is a moving object that is not divided into smaller parts during the transport process (e.g. passenger, shipment, wagon).
The dose is a summary of several elements that move together in a certain phase of the transport process (e.g. a group of passengers from Košice to Žilina, a group of freight wagons with a common starting and destination station).
The complete set is an object capable of separate movement in the transport process (e.g. a car with a driver, a train with train crew and prescribed markings).
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 8: 2. Basic terms of ITS with focusing on transport problems
The set is a dose created according to certain rules. After completing the specified objects (requisites) it creates the complete (e.g. a bus without a driver, train set without locomotive and train crew).
The requisites are the objects that need to complete the set to create the complete set (e.g. a bus, a service wagon, a train crew, a bus driver).
Transport hub is a place where at least one of the following options occurs:
elements enter the system,
elements exit the system,
collecting elements,
creation or manipulation of complete sets (e.g. public transport stop, railway stop or station, marshalling yard, crossing in road transport)
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 9: 2. Basic terms of ITS with focusing on transport problems
The section is the oriented link of two transport hubs that does not contain another hub (e.g. part of the railway line between adjacent railway stops considered for one direction of journey).
Throughput efficiency is the maximum number of complete sets that can pass over the time unit from the initial transport hub to the inside of the section (for example, the maximum number of vehicles that may leave the crossing in a given direction per time unit). Throughput is the property of only a given section and does not depend on the situation in other parts of the transport network.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 10: 2. Basic terms of ITS with focusing on transport problems
The transport network is the final set of interconnected transport hubs and sections. Each section has a given throughput efficiency and length, expressed either in length units or as the time required to pass the section (e.g. the network of public transport lines in Bratislava, the ŽSR railway network, as well as their parts).
The route is a sequence of transport hubs and the successive sections between these hubs (e.g., a vehicle that moves along a certain route when operating a group of stores). This does not exclude crossing the sections and transport hubs multiple times.
The track is a route whose transport hubs are two different (for example, the section of the railway network from Žilina to Čadca is a track in the sense of the established terminology: it is continuous, oriented and therefore it is a route where no transport hubs are repeated on it).
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 11: 2. Basic terms of ITS with focusing on transport problems
The relation is arranged with a pair of transport hubs, from the first to the second hubs being transported complete sets (e.g. the relation Banská Bystrica - Zvolen in the passenger transport).
The starting point of the element is the transport hubs in which the element enters the transport network.
The goal of the element is the transport hubs in which the element emerges from the transport network and its transport over that network ends here.
The source of a set of elements is a hub that is the common starting point of all the elements of that set.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 12: 2. Basic terms of ITS with focusing on transport problems
The position of the element at time t is the hub or section in which the element is at that point in time. Specifically, the designation of a hub or section by a given name or symbol is considered an address. The element's position at that point then indicates the current address of that document.
The center is a hub with a specific mission (e.g. railway yard, railway repair shop, ...). The above word definition of the center should be understood in relation to the model in which the hub is considered a point. In a more detailed model, the center may be part of a transport hub.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 13: 2. Basic terms of ITS with focusing on transport problems
The yard area of the center is precisely that part of the transport network in which this center fulfills its specific mission. The center itself is part of its yard area, in which is usually not another center with the same function. Yard areas of different centers with the same function do not usually overlap (this does not apply to the yard area of the railway yard for locomotives).
The transport link is a gradual transfer of complete sets along a route between two transport hubs (e.g. train passage from Nové Zámky to Štúrovo).
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 14: 2. Basic terms of ITS with focusing on transport problems
Intelligent transportation system (ITS) is an advanced application which, without embodying intelligence as such, aims to provide innovative services relating to different modes of transport and traffic management and enable users to be better informed and make safer, more coordinated, and 'smarter' use of transport networks.
Although ITS may refer to all modes of transport, the directive of the European Union 2010/40/EU, made on the 7 July 2010, defined ITS as systems in which information and communication technologies are applied in the field of road transport, including infrastructure, vehicles and users, and in traffic management and mobility management, as well as for interfaces with other modes of transport.
ITS may improve the efficiency of transport in a number of situations, i.e. road transport, traffic management, mobility, etc.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 15: 2. Basic terms of ITS with focusing on transport problems
Intelligent transportation technologies consist:
basic management systems such as car navigation;
traffic signal control systems;
container management systems;
variable message signs;
automatic number plate recognition or speed cameras to monitor applications, such as security CCTV systems;
more advanced applications that integrate live data and feedback from a number of other sources, such as parking guidance and information systems;
weather information;
bridge de-icing systems;
etc...
Additionally, predictive techniques are being developed to allow advanced modelling and comparison with historical baseline data.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 16: 2. Basic terms of ITS with focusing on transport problems
Intelligent transportation applications deal with:
Emergency vehicle notification systems;
Automatic road enforcement;
Variable speed limits;
Dynamic traffic light sequence;
Collision avoidance systems;
etc...
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 17: 2. Basic terms of ITS with focusing on transport problems
The Network of National ITS Associations is a grouping of Europe national ITS interests. It was officially announced 7 October 2004 in London. The secretariat is at ERTICO – ITS Europe.
ERTICO – ITS Europe is a public/private partnership promoting the development and deployment of ITS. They connect public authorities, industry players, infrastructure operators, users, national ITS associations and other organizations together. The ERTICO work programme focuses on initiatives to improve transport safety, security and network efficiency whilst taking into account measures to reduce environmental impact.
Intelligent Transport Systems: New ICT based Master’s Curricula in Uzbekistan (INTRAS) AGREEMENT NUMBER – 2017-3516/001-001 Project reference number – 586292-EPP-1-2017-1-PL-EPPKA2-CBHE-JP

## Slide 18: Thank you for your attention
contact: jaroslav.masek@fpedas.uniza.sk